1. Situation

Multiple BMS is boards is upon us. One BQ (currently smoked), one MX (sort-of-works), one ‘1818 (cell 1 & 2 acting funny), two ‘1818 almost completed. Soon three ‘1818 boards should be “somewhat-workable). Constructing another MX board using a Mouser sourced part is planned, and lastly refurbishing the blown BQ is on the todo list. Sorting out the scheme for handling CAN loading is needed. Here are some thoughts and initial work on scripts.

Each pcb board with a CAN node is given a CAN ID that is essentially permanent. It could be called a board serial number, but if serial numbers are assigned then a table to associate serial number with CAN ID is needed. Using the CAN ID seems a bit simpler amd cangate output shows CAN IDs so serial numbers complicates things.

For the current effort the number of pcb boards will be around 50. Approximately 20 will be generated for the BMS. There are a number of existing boards such as the POD board with CAN interface for use with load cells. Other boards, which will probably not see winch use, but might end up on the CAN bus, exist that have CAN IDs assigned. The SQL file CANID_INSERT.sql has a list. Currently 36 non-BMS IDs are assigned.

A PC will be access the CAN bus via a gateway making use of hub-server, socat, etc. Most of the CAN nodes will have CAN loader ability, but a few may not and require manually connecting a JTAG or ST-LINK SWD to load or update.

The update procedure would be for the Op to launch a program on the PC, then cycle either the 12V CAN power which causes all the units to reset/boot, or presses a button to cycle the reset line in the CAN cable which cycles the reset on those pcbs that have the CAN cable reset capability. The BMS boards currently are the only ones with that feature.

The application programs could also have their CAN routine check for a CAN msg that causes a software reset. This would avoid the need for causing a reset via hardware (i.e. power cycling, or reset line), but depends on the CAN node working correctly. If it is locked up the hardware reset is required.

When a board resets/boots, the CAN loader program starts and waits for a short duration. If no CAN msg associated with loading is received it jumps to the application program, provided that a checksum shows that the application program is present and good. If it receives a loading CAN msg the loading takes place. Following the loading, a software generated reset takes place and the loader waits for a short duration for a CAN loader msg.

With the PC accessing one CAN bus there isn’t much need to be loading multiple CAN nodes at the same time. Loading one CAN node at a time is sufficient. The time load the typical program is in the realm of 20 sec. Reloading twelve BMS nodes take 4 minutes.

2. CAN ID versus programs

The foregoing indicates that the PC needs a file that maps CAN ID to program(s) to be loaded. If the parameters and calibration factors are loaded separately from the application program, then they would be treated as just another program to be loaded.

The mapping file would need CAN ID, and the program directory for each program to be loaded to that CAN ID. Since file would have CAN IDs for units not connected to the CAN bus a flag for active entries would be needed so that the PC program could step through the entries that are active. But what about entries (i.e. CAN nodes) that do not need updating?

One approach would be to check a checksum on the program. The CAN loader could send the checksum and the PC checks that against the compiled program. If they match, the loading for that entry is skipped.

To avoid the need for cycling the power for each CAN node update, the CAN loader could be sent a “wait longer than usual” CAN msg. That way the CAN loaders would not jump to the application program when the previous unit was being loaded, and thus require cycling the power, or reset line, etc.

What if a CAN node doesn’t respond to the PC’s sending a “load” CAN msg?

Restarting the PC loader (and cycling the CAN bus reset) should have it begin where it left off, otherwise a re-try of the last guy on the list would required going down the entire list checking checksums. This might be fast, however. …

3. Function struct locations

In the CAN node there are several schemes for organization. In all schemes the CAN program loader would be in low flash, e.g. the first 0x5000 of flash.

The application may have several functions. Each function has a struct with the parameters specific to the function and board (e.g. ADC calibrations).

Flash addresse for each function is defined in the .ld file.

Several ways to deal with the function structs--

a. Combine app prog and function structs
    Any parameter update requires full program load (more time consuming, but not excessive).

    Compiling is simply compiling the program with an environmental variable that selects the function for that particular CAN ID.

b. App prog and each function struct has a designated flash section

    Each struct is compiled like a program and loads as if it were an executable program.

    The .ld file supplies the address of the struct. There would be unused flash space between sections.

c. App prog and combined function structs

    This is similar to b) but would combine the function structs into one flash section. This complicates how the app program gets the address of a function struct that follows the first struct. The first struct’s address would come from the .ld file, but the following ones depend on the size of the first, etc.

Compile before running a CAN update, or have the CAN update compile just before loading?

Most updates for the BMS would be program updates so having separate parameter and program updates won’t save much time. Calibration changes for the BMS will be rare. More likely is the program and how it handles charging, storage, balancing, etc.

4. Working struct initialization

The present approach initializes the function struct in SRAM by calling a subroutine that loads the struct with values. E.g. see--
~/GliderWinchItems/BMS/bmsadbms1818/Ourtasks/bq_func_init.c and .h

This simplifies the loading of the struct rather than coding the values by position into the struct where it is easy to make a mistake, e.g. something like this:

struct BQFUNCTION bqfunction = { <values> ...{struct within struct values},... };

Rather than have the function structs combine with the app, (a. above), this routine could be loaded in high flash and called by the app. The problem with getting the address of multiple functions is the same as before.

Combing the structs with the app (a. above) is the simplest, but assumes the time to update is not unreasonable.

5. How to do approach 3. a.

At top level: Master file, entries for each assigned CAN ID--
    CAN ID
    directory for app program

The app program directory has a script to execute the instances, e.g. the following script ‘run-instances’ located in ../BMS/bmsbms1818, compiles two instances of bmsbms1818--
#!/bin/bash
# run-instances
./mm B0A00000
./mm B0C00000

In this example run-instances mm passes the CAN ID to the mm script which passes it into make which selects the struct initialization for that CAN ID instance.

#!/bin/bash
# Example: Specify CAN ID to select parameters
# e.g. CAN ID = BOA00000
# ./mm BOA00000

rm build/bms1818.elf
export FLOAT_TYPE=hard

# Parameters for CAN ID specified by $1
export ADC_PARAM=$1-adc_idx_v_struct.c
export BQ_PARAM=$1-bq_idx_v_struct.c
echo $ADC_PARAM $BQ_PARAM

./script-all bms1818

Parameter file:
    ../function_params/B0800000
deh@ASUS:~/GliderWinchItems/BMS/bmsadbms1818/params$ ls -l
total 40
-rw-rw-r-- 1 deh deh 5808 Aug 20 21:25 B0A00000-adc_idx_v_struct.c
-rw-rw-r-- 1 deh deh 11991 Aug 20 21:25 B0A00000-bq_idx_v_struct.c
-rw-rw-r-- 1 deh deh 5808 Aug 20 21:25 B0C00000-adc_idx_v_struct.c
-rw-rw-r-- 1 deh deh 11991 Aug 20 21:26 B0C00000-bq_idx_v_struct.c

CAN update would go through Master file, skipping entries that either have a flag to skip, or have a checksum match when the unit is polled. In the directory with the program, the parameter file would be looked up on the CAN ID. That entry would be used to access the

 Executing the script “mm” runs the usual compile scripts. By setting an enviromental variable before doing a ./mm, ‘make’ will use the selected parameter file. E.g.--

mm file:

#!/bin/bash
# Example: Specify CAN ID to select parameters
# e.g. CAN ID = BOA00000
# ./mm BOA00000

rm build/bms1818.elf
export FLOAT_TYPE=hard

# Parameters for CAN ID specified by $1
export ADC_PARAM=$1-adc_idx_v_struct.c
export BQ_PARAM=$1-bq_idx_v_struct.c
echo $ADC_PARAM $BQ_PARAM

./script-all bms1818

In ‘Makefile’ –
...
C_SOURCES += params/$(ADC_PARAM)
C_SOURCES += params/$(BQ_PARAM)
…

In app directory, the parameter intialization .c files (in this example) are located in ../bmsadbms1818/params directory, e.g.--

deh@ASUS:~/GliderWinchItems/BMS/bmsadbms1818/params$ ls -l
total 40
-rw-rw-r-- 1 deh deh 5808 Aug 20 21:25 B0A00000-adc_idx_v_struct.c
-rw-rw-r-- 1 deh deh 11991 Aug 20 21:25 B0A00000-bq_idx_v_struct.c
-rw-rw-r-- 1 deh deh 5808 Aug 20 21:25 B0C00000-adc_idx_v_struct.c
-rw-rw-r-- 1 deh deh 11991 Aug 20 21:26 B0C00000-bq_idx_v_struct.c

Since the compile time for a different set of parameters is about 1 second, there is no need to compile before starting a CAN update. The compile can take place just before each CAN node update is attempted. Compiling for a change in the Makefile where everything, including unused HAL routines takes longer, but only is done once, so following nodes using that program would compile fast.

If there is just one CAN node involved the compile would still take place, but it would only take a fraction of a second.

So, compile-just-before-update is a reasonable approach.

There needs to be a check in the script to blow the whistle if a compile fails.

6. The run-instances script would need include CAN loading

The foregoing example executes mm which compiles and loads the program via the ST-LINK jtag. Makefile would need to be modified to only compile and run-instances script would need to call a routine that loads the .srec via CAN ID of the instance.